## Slide 1: Finite State Machine and it’s Application
A finite state machine(FSM) is a mathematical model of computation. It is a abstract machine that can be in exactly one of the many finite states at any given time. The FSM can change from one state to another state in response to some inputs. The change of state is called transition.
Presented by
Ammaar Ahmad
Roll No. - 1801CS08
Course- CS226(Switching Theory Lab)

## Slide 2: Topic of Discussion: Traffic Light Control System using FSM

## Slide 3
RED: Vehicles need to stop and wait until the signal is GREEN.
YELLOW: Vehicles should stop if they can safely put breaks. Soon the signal will be RED.
GREEN: Vehicles are allowed to move in particular direction such as Right, Left or Straight as a signal allows.
Basics of Traffic Light Control System

## Slide 4: Defining Different States
Name | Binary Code | East/West | North/South
S0 | 00 | Green | Red
S1 | 01 | Yellow | Red
S2 | 10 | Red | Green
S3 | 11 | Red | Yellow

## Slide 5: Terminologies
QA : Current State of the Second Flip Flop
QB : Current State of the First Flip Flop
QA* : Next State of the Second Flip Flop
QB* : Next State of the First Flip Flop
X : Output is 1 every 16 seconds.
Y : Output is 1 every 4 seconds.
Z : Output is 1 when no car in green signal road for 4 consecutive seconds.
OUT : Output is 1 to change the state of traffic signal
TA and TB: Input provided to respective Flip Flop

## Slide 6: State Transition Diagram
S0
00
S3
11
S1
01
S2
10
X=1, Z=0
Y=1, Z=0
X=1, Z=0
Y=1, Z=0
Z=1
Z=1
Z=1
Z=1

## Slide 7: Truth Table
QA | QB | X | Y | Z | QA* | QB* | OUT | TA | TB
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1

## Slide 8
QA | QB | X | Y | Z | QA* | QB* | OUT | TA | TB
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1

## Slide 9: Transition from one state to another
Transition occurs when Z=1, from RG to GR and vice versa. Or when X=1 from RG to RY and GR to YR. Or when Y=1 from RY to GR and YR to RG.
OUT = Z or X or (QB and Y)
TA = Z or (QB and Y)
TB = (Z and QB) or (~Z and X) or (QB and Y)
All Expressions have been obtained through Karnaugh map simplification(Not shown here)

## Slide 10: Ideas to improve on the project
We are checking whether there is car nearby to cross the road for 4 seconds. If no car is present then we are switching from RG to GR state. We can check for variable time depending upon time of Day to have better traffic system
Here Randomized variable is being used in implementation to check whether vehicle is nearby. In real life it can be checked with image processing to check the presence of car and switch accordingly.

## Slide 11
Implementation is done for 16 seconds between RG to RY state and GR to YR state. Time to change from one state to another state can be changed according to time of Day. Similarly time between YR to RG and RY to GR can be changed as required in complex implementation.
When the state is changed, for 1 second time counter stops and this leads to extra second for every state. This can be rectified.
Microcontroller can be used to make more efficient traffic light control system